IN HOUSE ENERGY COSTS CONTROL

IN THE TEXTILE INDUSTRY

Mian Fazal Ahmad *

Summary :

In the wake of galloping inflation, anticipated phenomenal rise in electricity tariffs in the coming years, it is imperative for the industry in Pakistan to drastically plan new strategies & techniques to meet this challenge. Staying competitive in the local & international markets as well as maintaining reasonable profitability are very important for future survival & growth of industry in Pakistan including the textile sector due to its vital role in the national economy.

Basic Factors :

The following major factors go to seriously affect economies of various costs in an industry.

- Electrical equipment & distribution system review & control.

- Better power load management.

  - Power factor, load factor & diversity factors control.

- Tariffs & commercial applications review and monitoring.

- Steam systems and management control.

- Buildings heat insulation for AC load economy.

- Wastes heat recovery & utilization.

An input/output model on subsequent page summarize the whole exercise involved in energy costs economies. Annexure I, II, Ill give further supporting information on these factors. Actual power factor improvements, load diversification and load management reviewed can pay substantial dividends in . terms of economy in energy costs.

* Mian Fazal Ahmad, B.Sc. Engg., Sr. MIEEE (USA), LLB, is a professional engineer with all round experience of over 40 years in management and engineering. Hi is currently Chairman Standing Committee Lahore Chamber of Commerce & Industry & is also CEO – Bureau of Quality Management.

INPUT / OUTPUT MODEL FOR ENERGY ECONOMY IN INDUSTRY

Electrical System costs																																		        Optimization																																																																																																										                   											  Economy in AC loads	                                                                             																																																																																																			                      Steam System																																		 Management & Control																																																																																																																																																																																													Model designed by Epsilon Engineering International (Pvt.) Limited

Energy Audit & Costs Optimization :

The concept of energy audit with a view to achieve cost optimization without sacrificing productivity in industry is now becoming a growing necessitity. To achieve effective audit & costs control, it is imperative to install proper management & technical system in an industry. The salient steps as highlighted in a flow chart are mentioned below;-

- Top management decision making for the specific objectives is essential to achieving effective results. Such a high level commitment is a basic requirement.

- An energy audit & control team (EACT) may be appointed which may comprise of electrical/mechanical engineers incharge, finance managers and manager administration. Specific tasks have to be assigned to them.

- The technicians concerned with the operation & maintenance of electrical and mechanical equipment should get training sessions on regular basis.

- The EACT mentioned above may first carry out initial assessment of the technical deficiencies in the industrial system.

- Based on the survey, a work plan for energy costs control & cost estimate for implementation should-be prepared.

- The EACT would be made responsible to ensure implementation of the energy costs control plan.

- The EACT should be a standing team to carry out continuous monitoring & surveillance of energy costs control.

The preliminary survey of deficiencies mentioned above would inter alia, cover :

- Review of the sizes & insulation conditions of all cables. Check leakage & overheating.

- Earth test values for motors and the cables.

- Check joints overheating.

- Load balancing in distribution layout as far as possible.

- Check power factor of motors and the overall extent of reactive power in the system.

- Check adequacy or over-rating of motors viz-a-viz, the mechanical load requirements as well as overheating.

- Check maximum demand optimization through better diversity factor and optimum equipment sizing.

- Check proper tariff application and load management methods.

- Check areas of steam wastage & conservations per Annexure II.

- Check unnecessary load for air-conditioning by improving insulation system.

Flow Chart for

Energy Audit & Costs Optimization in Industry

Model designed by Epsilon Engineering International (Pvt.) Limited

Annexure I

A study of the industrial and commercial sectors of Pakistan found a substantial potential for electricity savings. The two combined sectors have a cost-effective savings potential of 30% of their projected electricity consumption in the year 2005. These savings translate into 25000 GWh of avoided electricity generation. Likewise, there is a scope for large reduction in the expansion of the power supply system. The potential reduction in base load generating capacity is 3200 MW and the reduction in intermediate and peak capacity is close to 4000 MW.

In the industrial sector, the savings potential of 8600 GWh is 21% of the projected consumption in the year 2005. Additionally, 1400 MW of base generating capacity as well as 800 MW of peak capacity can be saved as a result of greater end-use efficiency in the industrial sector. Electric motors are the dominant load in industry with an estimated 80% of total electricity consumption. Electric motors that are made by large manufacturers in Pakistan have similar characteristics to the motors made in developed countries. However, motors made by small industries are of low efficiency.

Table 1 shows the breakdown of industrial savings by technology. All the conservation technologies are cost effective, with the possible exception of electronic speed controls. Speed controls present the bulk of the industrial savings potential associated with speed controls is over 5000 GWh of electricity generated and over 800 MW of base generating power.

Pole-amplitude-modulated (PAM) motors, appropriate for applications where a few speeds are required, present excellent rates of return. Electronic adjustable speed drives (ASDs), appropriate for applications requiring continuous speed regulation, are not cost-effective for small drives. ASDs are attractive for large drives (>100 HP) in applications of 2000 hours or more per year. ASDs for. medium drives (15 HP to 100 HP) are only cost-effective if operating over 3500. hours per year.

Energy-efficient motors (EEMs) are cost effective, specially in new applications and can save over 1300 GWh of generated electricity and over 200 MW of base generating capacity in the year 2005. Load management is very cost effective means to reduce peak demand, presenting around 800 MW of savings potential. Power factor correction can reduce industrial consumption by over 3%, besides reducing voltage fluctuations and improving the capacity factor of the system. Power factor correction is also very cost effective.

The potential electricity savings in the commercial sector could reach 40% of the projected consumption in the year 2005. Lighting is the dominant load in the commercial sector with an estimated 70% share' in 1985. Table 2 shows the

savings breakdown by conservation technology. In the commercial sector,' improved lighting offers two-thirds of the potential electricity savings.

The combined application of high efficiency florescent tubes, high efficiency ballasts and compact florescent can reduce the lighting load by 28%, 6% and 15% respectively. These improvements are also cost effective and can save 11000 GWh of generated electricity. Additionally, they can avoid 1800 MW of base generating capacity.

Table 1
Potential Electricity Savings in Industry in the Year 2005

|  | Power Savings Base/Peak (MW) | Energy Savings at consumption (GWh) | Energy Savings at Generation (GWh)* |
| --- | --- | --- | --- |
| E. E. Motors | 220 | 1060 | 1340 |
| Speed Controls | 840 | 4100 | 5190 |
| Lighting | 110 | 530 | 670 |
| Load Management | 830 |  |  |
| Power Factor | 230 | 1140 | 1440 |
| Total | 1400/830 | 6830 | 8640 |

Notes:

-	* Includes 21% losses

-	** Non-diversified peak at consumer point

Table 
Potential Electricity Savings in the Commercial Sector in the Year 2005

|  | Power Savings Base/Peak + Int. (MW) | Energy Swings at consumption (GWh) | Energy Savings at Generation (GWh)* |
| --- | --- | --- | --- |
| Florescent Tubes | 1020 | 5000 | 6330 |
| High Efficiency Ballasts | 230 | 1140 | 1440 |
| Compact Florescent | 550 | 2640 | 3340 |
| Fans | 270 ** | 320 | 400 |
| Room Air Conditioners | 1100 ** | 1300 | 1650 |
| Thermal Insulation | 2000 ** | 2400 | 3030 |
| Total | 1800/3370 | 128d0 | 16200 |

Notes:

-	* Includes 21% losses

-	** Non-diversified summer peak and intermediate generating capacity

Air conditioning loads are expected to grow substantially in the next two decades, increasing their share of the overall commercial load from the present 15% to 30% in the year 2005. The use of thermal insulation can cut the cooling load by one-third, providing an immediate payback due to savings in the air conditioning capacity. The use of thermal insulation, can save over 3000 GWh of generated electricity and over 2000 MW of intermediate and summer peak generating capacity.

High efficiency room air conditioners are not very cost-effective to the consumer, although their savings potential is considerable. They can save 1600 GWh of generated electricity and over 1000 MW of intermediate and summer peak generating capacity. The following actions are recommended to tap this savings potential.

- Development and promotion of an information and training program for electricity users about the availability and advantages of energy saving technologies.

- Establishment and enforcement of standards both for end-use equipment and buildings.

- Creation of incentives, for local manufacturers and consumers, to promote the penetration of high efficiency equipment in the areas with large savings potential. Some industries, namely the small industries , may also need technical assistance.

- Establishment of time use rates, reflecting the true costs of power and energy to promote load management.

- Promotion of the availability of good quality materials, namely silicon steel, at a reasonable cost for the local producers of electricity consuming equipment.

Steps for Conserving Electrical Energy in any Plant or Facility

A number of steps are offered below as guideline to achieving energy savings in any facility.

1.	Understand the electricity tariff and bill

- Is the proper tariff being applied?

- What are the marginal costs of demand and consumption?

- Is the billing accurate?

- What is the maximum demand?

- Is there a power factor penalty?

- What is the plant load factor?

2.	Monitor, measure, and record electricity consumption/demand

- What is the monthly variation in consumption and demand?

- Can differences in billing from month to month be explained?

- What is the electricity consumption in major plant areas or processes?

- What are the major electricity-consuming machines or equipment?

- Which machines or equipment make the greatest contribution to maximum demand?

- At what time of the day does maximum demand occur?

- Has an electrical energy budget or audit been performed?

- What is the electricity consumption per unit of production?

- What instruments are available in the plant?

- What readings and measurements are normally taken.

3.	Maintain and upgrade electricity distribution system

- What is the condition of the distribution system?

4.	Use efficient electrical equipment

- What is the age and condition of electrical equipment in use?

- What maintenance is regularly performed?

- How old are the motors?

- How many times have the motors been rewound?

- What light sources are in use?

- What are the efficiencies of the pumps and compressors?

5.	Operate and apply electrical equipment efficiently

- Is the equipment properly sized for the application?

- Does the equipment normally operate fully loaded?

- Can air flows or pump flows be reduced in any cases?

Steps to Heat Recovery Project Implementation :

- Identify potential sources of waste heat.

- Evaluate the heat content of the water heat sources.

- Determine possible applications for waste heat.

- Match waste heat sources to the right applications.

- Select a possible method/equipment configuration for heat recovery.

- Evaluate energy and cost savings potential of waste heat.

- Develop a budget cost estimate for implementation:.

- Evaluate return on investment.

- Perform detailed study and analysis.

- Implement the heat recovery project.

Annex-II

Checking Steam System Operation

The "energy performance" of a steam system may be evaluated by testing the system for;-

- Steam pressure & temperature

- Improperly functioning steam traps

- Condensate recovery

- Leaks and missing or damaged insulation

Taking the boiler and steam distribution system together, it is often useful to ask the following questions;-

Steam Generation

- Do we have the right boiler(s)?

- Are the boilers working efficiently and correctly?

- Are the fuel and steam metered? For each boiler?

- Are the feed tank arrangements satisfactory?

- Is blow-down under control?

Steam Distribution

- Is the system layout as good as it should be?

- Is the system effective?

- Is steam trapping satisfactory on steam mains?

Steam Utilization

- Is the equipment used properly?

- Are temperature properly controlled?

- Is drainage and air venting correct?

- Do the steam traps waste steam?

- Are steam traps working?

Condensate Handling

- Is condensate properly used?

- Are there other losses or problems?

- What about flash steam?

DEFINITIONS

Load factor of losses: The ratio of the average power loss of a transformer calculated over a stated period to the power loss in the transformer when working on the maximum load demanded from it at any time during that period.

Maximum demand: The maximum current, power or volt-amperes supplied to a consumer during a prescribed period. The power maximum demand usually employed is determined by integrating the power during successive equal intervals of time and recording the highest. The duration of the interval usually prescribed is half an hour.

Load factor: The ratio of the total number of kilowatt-hours supplied to a consumer during a given period to the total number of kilowatt-hours which would have been supplied if the maximum demand had been maintained throughout the year.

Diversity factor: The ratio of the arithmetical sum of the individual maximum demands of the components of a group of power supplies to the simultaneous maximum demand of the group.

IN-HOUSE ENERGY AUDIT

FOR

CUTTING O & M COSTS IN INDUSTRY

EVALUATION FORM

(Designed by Bureau of Quality Management)

(Rights Reserved)

Form No. BQM/EA/02

|  | Yes | No | Remarks |
| --- | --- | --- | --- |
| Management Key Factors: Is the top management committed to Energy Costs Economy. Is there an Energy Audit & Implementation Team within the Organization to take practical steps for O&M Costs Cutting? |  |  |  |
| Technical Measures: Have you checked sizes & insulation conditions of all cables ? Any detected leakages in the cables ? Any overheating in the cables ? Earth Test Values of Motors ? Earth Test Values of Cables ? Checked joints overheating & looseness ? Are the joints tight/well compressed and worn-out cables replaced? Is the load distribution balanced on all phases ? Have you checked power factor of motors and prepared plan for raising it to 0.85 to avoid excessive flow of current and reactive losses? Are the motors overrated matching the required mechanical loads? If so, are corrective steps planned to avoid over billing due to excess loads ? Have you adjusted unnecessary maximum demand through better diversity factor MDI Controller and optimum equipment sizing ? Have you installed harmonics clearing equipment for better quality of incoming power supply ? Have you scrutinized and checked proper tariffs application to avoid over billing after better load management ? Have you examined application of economical TOD Tariffs ? Have you checked areas of steam wastages and adopted conservation measures through efficient Boilers, steam Generation, Distribution and utilization methods? Have you check unnecessary loads for Air-Conditioning by improving Heat Insulation System ? Have you planned to replace high loss materials and low efficiency equipment in your installation ? Is there waste heat in the industrial process and have you planned to co-generate extra power by recycling waste heat ? To plan and implement Energy Costs reduction measures through In-House Audit, have you sufficiently trained manpower in your setup ? Have you prepared definite plans for implementation under professional supervision after a cost benefit analysis through In-house arrangement or engagement of outside Consultants ? |  |  | Are these within limits? Are these within limits? |

# Text boxes

Load Management in industry

Tariff & Commercial Monitoring

Better Heat Insulation in Buildings

Steam Generation

Steam Distribution

Steam Utilization

Waste Heat Recovery & Utilization

ENERGY ECONOMY

Technical & Management System

Economized  Energy Costs

Equipment & Dist. Layout Design Control

Economised  Energy Costs

Continued Evaluation of Costs Control Operation

Work Plan & Costs Estimation

Implementation & Monitoring

Appoint Energy Audit & Implementation Team

Preliminary Assessment of Deficiencies

Top Management Decision

International Conference on Textile and Clothing – 4, 2013

Sustainable Products & Textile Exports

28th – 29th – 30th March, 2013 Expo Center, Lahore